## Slide 1: MGT 207
Quality Management and Statistical Process Control

## Slide 2: Natural Manufacturing Variations

## Slide 3: All Processes Have Some Variation… But There Is Typical Variation and Atypical Variation
Time
Application number
For example, the time taken to rate an insurance policy …
What would you think if the time to rate a particular policy took 40 minutes
20 min
Notes: All operations involve some sort of processes, whether it’s a production process to manufacture tangible goods, or it’s a service process to provide intangible service. One you have process, you’ll face variations.

## Slide 4: Process is In-Control if Measurements Fall Within the Typical Range
Time
Application number
This process is staying in control
20 min
In-control does not necessarily mean high quality, it just means the process is behaving as you expect it to behave

## Slide 5: A Change In Measurements Indicates Process May Be Out-of-Control
Time
Application number
A significant change indicates that the process is no longer behaving as you expect it to behave
20 min
Notes: What is significant change and what is not – this all seems too subjective. Yes, indeed so far we haven’t been able to what is an atypical change in a process, that’s where we need statistical techniques – next, I’m going to introduce a method that will allow us to objectively decide what is an atypical change, in other words, allow us to tell the difference between acceptable and inacceptable variation.

## Slide 6: Quality Testing by Sampling
Goal: to see if there is …
  A shift in process mean
  An increase in process variation
A sample is a set of measurements
For example
  Sample frequency = every 5 products
  Sample size n=4
Inspection
Sample 1
Sample 2

## Slide 7: Some Examples of Sample Data…
Sample (Inspection) | Measurement |  |  |  | Sample Mean | Range (max-min)
 | 1 | 2 | 3 | 4 |  | 
1 | 97.06 | 97.32 | 100.19 | 101.02 | 98.90 | 3.96
2 | 97.68 | 100.05 | 97.80 | 97.85 | 98.34 | 2.37
3 | 98.76 | 98.22 | 100.72 | 103.11 | 100.20 | 4.89
4 | 101.34 | 100.00 | 103.19 | 105.79 | 102.58 | 5.79
5 | 102.78 | 105.28 | 105.02 | 97.96 | 102.76 | 7.32
6 | 104.23 | 104.57 | 97.50 | 100.39 | 101.67 | 7.07
Notes: Vertically list all samples
Horizontally list all measurement in a particular sample.
Tabulate the means for each sample
Tabulate the ranges for each sample

## Slide 8: Visualizing the Data Can Be Helpful
A plot of sample means
Sample
Sample Mean
Notes: This is a scatter plot

## Slide 9: Let’s Look at the Next Sample Mean
Say Sample 7 comes in with a mean of 85
Sample
Sample Mean
How might you decide if 85 is atypical for this process?

## Slide 10: One Approach Is to Specify Limits on What Is Typical
Anything outside the limits is considered abnormal
Think of the Sample Means being Normally Distributed
Notes: Central limit theorem: sample average is normally distributed around the true average or population average and the variability depends on sample size.

## Slide 11: But What Are the Right Limits ?
Wide or Narrow?
Pros and Cons of Wide or Narrow
Narrow
Wide
Pro:
Con:
Pro:
Con:
Wide ?
Narrow ?
Notes: Type I vs Type II error:
When limits are too narrow, you may have false alarms too often, i.e., making too many type I errors.
When limits are too wide, you may have overlooked problems, making type II errors
Link to appraisal costs vs. external failure costs.

## Slide 12: Often the Limits Are Set As Mean +/- 3 Standard Deviation
Anything outside the limits is considered atypical
UCL: upper control limit
LCL: lower control limit
Center Line = Mean
3 x Standard deviation
3 x Standard deviation
Notes: Three Sigma quality level translates to a process yield of 99.73% yield.

## Slide 13: How Many Defects Per Million?
Mathematical Representation:
Calculate Z-Scores:
For +3 Standard Deviations: =NORM.S.DIST(3,TRUE)
For -3 Standard Deviations: =NORM.S.DIST(-3,TRUE)
Calculate Probabilities Outside Limits:
=1 - (Z-Score for +3) + (Z-Score for -3)=1-0.9986+0.001349
Convert to the Number of Defects per Million Units Produced:
= 1E06*(1-0.9986+0.001349)=2,700.

## Slide 14: What mean and standard deviation should we use ?
Sample Means’ Mean
The mean of the sample means
Sample mean for the ith sample
Number of samples
Sample Means’ Standard Deviation
The standard deviation of the sample means
  Can be estimated as the standard deviation of an individual measurement (i.e. the process standard deviation) divided by square root of n, the sample size
Sample size
Process standard deviation

## Slide 15
Calculating Process Standard Deviation
Process Standard Deviation
A constant that can be found in tables
The average value (mean) of the sample ranges

## Slide 16: Bringing It All Together
A constant that can be found in tables
Mean of the sample means
Mean of the sample ranges
Control Limits = Mean of Sample Means +/- Constant x Mean of Sample Ranges
UCL: upper control limit
LCL: lower control limit
Mean
3 x Standard deviation
3 x Standard deviation

## Slide 17: Table for A2 constants
Sample size is the number of measurement in each sample and NOT the number of samples

## Slide 18: Calculate the Center Line, UCL and LCL for the following set of data
Sample | Measurement |  |  |  |  | Mean | Range
 | 1 | 2 | 3 | 4 | 5 |  | 
1 | 49.59 | 53.94 | 47.11 | 60.58 | 43.48 | 50.94 | 17.10
2 | 60.41 | 48.90 | 29.19 | 58.87 | 39.80 | 47.44 | 31.22
3 | 65.89 | 56.96 | 44.15 | 60.76 | 50.39 | 55.63 | 21.74
4 | 48.48 | 51.02 | 57.36 | 45.54 | 63.11 | 53.10 | 17.56
5 | 49.10 | 40.69 | 42.10 | 29.26 | 46.40 | 41.51 | 19.84
6 | 42.76 | 35.11 | 47.66 | 46.78 | 44.93 |  | 

## Slide 19: Center Line, UCL and LCL
UCL
LCL
Center Line

## Slide 20: Consider the Following Samples Is the Process In-Control?
Sample | Measurement |  |  |  |  | Mean
 | 1 | 2 | 3 | 4 | 5 | 
101 | 36.62 | 50.01 | 44.39 | 35.84 | 50.41 | 43.45
102 | 42.91 | 34.72 | 54.82 | 51.67 | 56.01 | 48.03
103 | 57.50 | 49.69 | 69.49 | 43.18 | 51.50 | 54.27
104 | 58.36 | 53.28 | 55.59 | 59.06 | 41.70 | 53.60
105 | 30.22 | 16.00 | 51.87 | 44.67 | 94.27 | 47.40
106 | 2.92 | 28.45 | 76.67 | 66.05 | 29.04 | 40.63
All means fall within the control limits so the process mean has not shifted

## Slide 21: Plotting the Sample Means
Sample means all fall within control limits
Sample
Sample Mean
LCL
UCL
Centerline
Notes: Talk about how to draw UCL and LCL, center line using excel.

## Slide 22: X-bar Charts Capture Shift in Means But Not Shift in Variability
X-bar would capture the following process shift
Original process
Process undergoes a shift in the mean
The shift would be noticed as the sample means would start to fall outside the control limits
X-bar would not capture the following process shift
Original process
Process mean stays the same but process becomes more variable
The shift would NOT be noticed as the sample means would still fall within the control limits

## Slide 23: Range charts
Measuring Shifts in Variability

## Slide 24: Range Charts (R-Charts) Are Used to Capture Shifts in Variability
Anything outside the limits is considered atypical
UCL: upper control limit
LCL: lower control limit
Mean range
How Do We Set the Control Limits
Calculate the Mean Range
1
Calculate the Control Limits
2
D3 and D4 are constants that can be found in tables
Notes: Similarly, we have UCL and LCLs

## Slide 25: Table for D3 and D4 Constants
Sample size is the number of measurements in each sample and NOT the number of samples

## Slide 26: What are the R-Chart Control Limits for This Process?
Sample | Measurement |  |  |  |  | Mean | Range
 | 1 | 2 | 3 | 4 | 5 |  | 
1 | 49.59 | 53.94 | 47.11 | 60.58 | 43.48 | 50.94 | 17.10
2 | 60.41 | 48.90 | 29.19 | 58.87 | 39.80 | 47.44 | 31.22
3 | 65.89 | 56.96 | 44.15 | 60.76 | 50.39 | 55.63 | 21.74
4 | 48.48 | 51.02 | 57.36 | 45.54 | 63.11 | 53.10 | 17.56
5 | 49.10 | 40.69 | 42.10 | 29.26 | 46.40 | 41.51 | 19.84
6 | 42.76 | 35.11 | 47.66 | 46.78 | 44.93 | 43.45 | 12.55

## Slide 27: Center Line, UCL and LCL Calculations
UCL
LCL
Center Line

## Slide 28: Consider the Following Samples Is the Process In-Control?
Sample | Measurement |  |  |  |  | Mean | Range
 | 1 | 2 | 3 | 4 | 5 |  | 
101 | 36.62 | 50.01 | 44.39 | 35.84 | 50.41 | 43.45 | 14.58
102 | 42.91 | 34.72 | 54.82 | 51.67 | 56.01 | 48.03 | 21.28
103 | 57.50 | 49.69 | 69.49 | 43.18 | 51.50 | 54.27 | 26.31
104 | 58.36 | 53.28 | 55.59 | 59.06 | 41.70 | 53.60 | 17.36
105 | 30.22 | 16.00 | 51.87 | 44.67 | 94.27 | 47.40 | 78.28
106 | 2.92 | 28.45 | 76.67 | 66.05 | 29.04 | 40.63 | 73.75

## Slide 29: Out of Control? Need to Look at Both X-bar Chart and R Chart
R Chart Shows the Process Has Gone Out of Control
UCL: upper control limit=42.21
LCL: lower control limit=0.00
Mean range
=20.00
X-bar Chart Looks like Process Is in Control
UCL: upper control limit=60.28
LCL: lower control limit=37.08
Mean
=48.68
Is it bad if a sample range falls below the LCL ?
Notes: no - it's good. it shows the variability has decreased

## Slide 30: In Class Exercise:
  Determine upper and lower limits for mean(X-bar) and range charts.
  Is the process in control?
measurements

## Slide 31: Solution
X-Bar Chart
R-Chart
Yes, the process is under control

## Slide 32: Process capability

## Slide 33: A Common Measure of Process Capability
Equation
process standard deviation
upper specification limit
lower specification limit
Cp > 1 : Process capable
Cp < 1 : Process not capable
Cp = 1 : Process borderline capable
Cp=1 i.e. USL-LSL=6σ
Disk Thickness
Prob. Density
Probability above USL=0.135%
Probability below LSL=0.135%
USL
LSL
Probability of Defect = 0.27%
Notes: Numerator: voice of the customer
Denominator: voice of the process
Don’t confuse USL/LSL with UCL/LCL
Cp increases -> lower defective rate
Cp = 1 -> 0.27% = 0.0027 = 2700 per 1,000,000

## Slide 34: Are the Following Processes Capable?
Process | Sigma | USL | LSL | Cp
A1 | 0.05 | 100.03 | 99.97 | 
A2 | 0.01 | 100.03 | 99.97 | 
B1 | 0.001 | 5.05 | 4.95 | 
B2 | 0.0005 | 5.05 | 4.95 | 
B3 | 0.02 | 5.05 | 4.95 | 

## Slide 35: Are the Following Processes Capable?
Process | Sigma | USL | LSL | Cp
A1 | 0.05 | 100.03 | 99.97 | 0.2
A2 | 0.01 | 100.03 | 99.97 | 1.0
B1 | 0.001 | 5.05 | 4.95 | 16.67
B2 | 0.0005 | 5.05 | 4.95 | 33.33
B3 | 0.02 | 5.05 | 4.95 | 0.83

## Slide 36: You Need to Be Careful With Cp
Cp=1 and Process Centered
Output
Prob. Density
Probability above USL =1-normsdist(3)=0.135%
Probability below LSL =normsdist(-3)=0.135%
USL
LSL
Probability of Defect = 0.27%
Cp=1 but Process Mean increased by 1.5σ
Output
Prob. Density
Probability above USL =1-normsdist(1.5)=6.68%
Probability below LSL =normsdist(-4.5)=0.00034%
USL
LSL
Probability of Defect = 6.68% !

## Slide 37: Another common measure is Cpk
Process mean
Calculate the Cp and Cpk for Process A2 if the mean is 100
Calculate the Cp and Cpk for Process A2 if the mean is 100.015
=0.5